Setting The System Clock on the Comdial DSU

You can program the system clock to maintain current date and time

Information. The time and date appear on the LCD speakerphone for

Display.

To set the system clock from the attendant’s station,

1. Press INTERCOM.

2. Dial * #0 1.

3. Dial two digits (00-99) for year.

4. Dial two digits (01-12) for month.

5. Dial two digits (01-31) for day.

6. Dial two digits (00-23) for hour.

7. Dial two digits (00-59) for minutes.

8. Press SPEAKER to end.

Programming The Attendant Features GCA70–245

2–14 LCD Speakerphone Reference Manual